## Slide 1
Phase 2: audit → re-measure → re-test
the question changed from 'which batch is different?' to 'which numbers can we defend?'
Every marker re-derived under the frozen Batch_3-fitted recipe; every claim re-graded
Sorted into a scorecard, not a verdict — MARKER_SCORECARD.md + AUDIT_LEDGER.md
  Tier A — validated descriptors (describe, don't discriminate)
  Tier B — candidate associations (real in crops, unprovable as material)
  Tier C — model-derived + correlation layer (fresh, corrected)
  Tier X — demoted/withdrawn (documented, not deleted)
9 defects reproduced and repaired on the way (contact denominators,
  BH step-up, NaN→p=0, channel masks, crack direction, QC weight leak…)
Deliverable = an evidence ledger — every number traced to file + test

## Slide 2
What survives: shared structure, one corrected ordering
Tier A — all three batches look like the same kind of material
marker | B1 / B2 / B3 | meaning
candidate-Si fraction | 0.0595 / 0.0614 / 0.0603 | ~6% Si everywhere — kills 'B1 excess Si'
resolved pore fraction | 0.104 / 0.108 / 0.109 | same resolved porosity
pore orientation S_dir | 0.585 / 0.563 / 0.573 | near-horizontal pores in ALL batches
pore contact (corrected) | 0.483 / 0.378 / 0.354 | B1 most connected — ordering, not activity
Si enclosed share | 0.720 / 0.778 / 0.781 | consistent: B1 least enclosed
low-coverage Si | 0.867 / 0.882 / 0.906 | 87–91% blind spot — sub-resolution pores
patchiness (hotspot) | 3.75 / 3.78 / 4.29 | equally patchy, no mega-cluster
Constraint: 0 markers clear the declared minimum-detectable-difference (v2 batch_differences: zero survivors)
dfn_output_v2/ · validated_comparison/ · orientation_analysis/ — corrected outputs, frozen recipe

## Slide 3
The confound, quantified — and the one survivor
predeclared benchmark: can any marker set classify batch?
protocol | best honest set | envelope | acq. signature | majority
leave-one-image-out | 51.6% | 59.3% | 61.3% ← wins | 54.8%
leave-group-out | 41.9% | 54.2% | 38.7% | 54.8% ← ties
The imaging-session signature alone beats the material envelope
  the pipeline sees the photography session better than the material
Corrected blind-test bookkeeping: 0/2 confirmed (3e→B1 was B2,
  fn→B2 was B1 — both flagged cant_tell_session_matched in advance)
Lone BH survivor: pores_per_mpx — B1>B3 +34.5 (p=0.0005),
  pore_d50 agrees (more, smaller pores in B1) — but B1–B3 share ONE
  matched image: real association, untestable confound
External 76–98% scores: documented as not ours
benchmark_results.csv · new_image_assignment/assignment_report.md · pairwise_comparisons.csv

## Slide 4
What was fixed or withdrawn
Tier X — retracted in the record, not hidden; archive/ARCHIVE.md
FFT 'vertical texture' — withdrawn: measured frame aspect ratio;
  replaced by validated S-parameter orientation (synthetic + null tested)
Crack-like metric — was selecting horizontal objects labeled vertical;
  two definitions still disagree → report per-definition or drop
Accessible-Si denominator bug — exemplar 0.524 → 0.371;
  renamed: resolved-pore-contact proxy, not activity
'Uncertain-bright ≥ Si brightness' — false in B1 after mask fix
  (InLens 1.395 < 1.459); true only in B3
Stats bugs — BH elementwise error, NaN→p=0, QC weight leak
  (redundancy fit on pooled batches) — all tables regenerated green
D10 particle size — grazing cuts fake small particles:
  demoted to 2-D profile diagnostic; tile-'jackknife' renamed tile SE

## Slide 5
Correlation layer + fresh DFN — and the honest headline
Tier C: model-derived indicators, not measurements
layer | result | reading
S2 correlation | pore len x/y anisotropy ≈1.5, all batches | independent confirmation of horizontal pores
PCF g(r) vs CSR | peak 5.4–7.2 at ~0.75 µm, above envelope | Si clustered beyond random — everywhere
DFN v2 stress | B1−B3 = −3.0 MPa (CI −6.02,−0.02) | meaningful-looking BUT inside assumption spread (IQR 3.9)
DFN capacity/swelling | below declared thresholds | no model-level difference
Same amounts (~6% Si, ~10% pores),
  horizontally-elongated pores, Si clustered beyond random), one real
  contact ordering in B1's favor — but the pipeline classifies the session
  better than the material: no batch/manufacturing difference claimable
What remains: validated descriptors + frozen honest ruler + preregistered
  blind-test protocol for the six incoming images + a ledger that shows its work
corr_analysis/ · dfn_output_v2/dfn_paired_differences.csv · BLIND_TEST_PROTOCOL.md